## Slide 1: د.زينب عبد الأمير
Instruments in gynecology

## Slide 2: Artery Forceps
used for
clamping bleeding vessels
grasping tissue at the time of operation( Opening and closing peritoneum)
hold stay sutures.

## Slide 4: Babcock's Forceps
The tip is atraumatic as there are no sharp tooth.
it used for grasping tubular structures like:
fallopian tube in tubectomy in modified Pomeroy's operation
Ureter
appendix

## Slide 5: ovum holding forceps
The tip of this instrument is rounded cup like to avoid perforation and to hold large tissue.
used for removing the products of conception in
inevitable
incomplete abortion
in termination of pregnancy operations.

## Slide 6: Allis' Forceps
used for grasping tough structures like
Rectus sheath
fascia
in operations like :
Tubectomy
LSCS
abdominal hysterectomy.

## Slide 7: doyen's retractor
used for retracting bladder downwards during abdominal operations like
.LSCS
abdominal hysterectomy
laparotomy

## Slide 8
Doyen's retractor

## Slide 9: deaver's retractor for retraction of deep structures

## Slide 10: kocher's forceps (clamp)
The tips of the blades have teeth so that the tissue does not slip.
The blades can either be straight or curved.

## Slide 11
This instrument is used in
holding pedicles in hysterectomy
salpingectomy in ectopic
oophorectomy in ovarian mass.
This can also be used for clamping umbilical cord of new born at the time of delivery
artificial low rupture of membranes ( ARM).

## Slide 14: Vulsellum Forceps
Types:
1. Single toothed (bullet forceps) Tenaculum
2. Double toothed (Fenton’s bull-dog vulsellum or the lion’s forceps)
3. Multiple toothed vulsellum (Tenaculum)

## Slide 15: vulsellum
This instrument is used for grasping the cervix ( Usually anterior lip of the cervix is grasped)
Its a long instrument with gentle curve so that the line of vision is not obstructed

## Slide 16
The tip of the blades have 3-4 teeth to hold and steady the cervix in procedures like
Insertion of IUCD
Cx Biopsy
D&C
First trimester TOP with Suction Evacuation
Vaginal Hysterectomy

## Slide 17
Posterior lip of the cervix is grasped for post. colpotomy .
Since the teeth are sharp it is not used in pregnancy as it may cause cervical tears and lacerations. Instead sponge holding forceps is used to grasp the cervix.

## Slide 18
PROCEDURE
Patient-lithotomy position
Posterior lip of cervix-downwards and forwards with vulsellum forceps
Speculum-retracts posterior vaginal wall
Area disinfected
Aspiration syringe inserted into the pouch and aspirated
Done best in OT under full asceptic precautions and to proceed laproscopy/laprotomy if indicated

## Slide 20: Indications:
1. Grasping of the cervix

## Slide 21
2. To grasp a prolapsed submucous myoma during a vaginal myomectomy.
3. During operation of hysterectomy it can be used to hold the cercal stump
after the removal of the uterine body in subtotal hysterectomy.

## Slide 22: Contraindications:
The soft pregnant cervix,
Infections,
Suspicious malignancy of the cervix.

## Slide 23: Complications:
1. Lacerations of the cervix.
2. Infections
3. Bleeding from the site of the bite of the teeth of the vulsellum

## Slide 29: surgical blades/ scalpel

## Slide 30: Bonney's myomectomy clamp

## Slide 32
BONNEY MYOMECTOMY CLAMP
It is applied on the lower part of the uterus just above the cervix to compress the uterine arteries to minimize blood loss during abdominal myomectomy.
The blades may cause crushing of the uterine wall.
Instead a rubber catheter is preferred because it is less traumatic and both uterine and ovarian arteries are occlude

## Slide 37: Sponge Holder / Sponge holding forceps
this is used for
holding sponge or a gauze piece for painting the area before operation.
for grasping the cervix in obstetrics in exploring cervix after forceps delivery ( three sponge holding forceps are used)

## Slide 42: shirodkars cerclage needle
This is specially designed needle for putting stitch around the cervix.

## Slide 43: Bladder Sound
It is long instrument with
gentle curve ( not angled like uterine sound)
has no markings on it.

## Slide 44
It is used to
define extension of bladder cystocele
vaginal hysterectomy.

## Slide 45: Uterine sound
Its a long instrument with blunt tip ( To avoid perforation) About 5 cms from the tip its bend to make angle of 30 degrees.
It has marking on it for measurements. ( Bladder sound has no markings )

## Slide 48
Uterine Sound
indicatlons
Diagnosis of cervical stenosis
it cannot be introduced through the cervical
(2) measure the length of the cervix by feeling resistance at the internal os.
This is of value in
diagnose supravaginal elongation in case of uterine prolapse
during Fothergill’s operation to estimate the length to be amputated

## Slide 49
(3) diagnosis of incompetent cervix. When internal os is wide the sound rocks
freely inside it

## Slide 50
4) measure the length of uterine cavity
This is done before dilatation of the cervix to avoide perforation of uterus
diagnose uterine hypoplasia

## Slide 51
(5) to know the position and direction of uterus as in Retroversion

## Slide 52
(6)Elicit the click sign in vesicovaginal fistula

## Slide 53
Contraindications:
1. Genital infections
2. Suspicion of pregnancy
3. Soft uterus (malignancy, infection, molar pregnancy).

## Slide 54
COMPLICATIONS
(1) Ascending infection
(2) Perforation of uterus
(3)Shock (Neurogenic shock) due to pain may occur in sensitive women
(4) Abortion may occur if introduced into a pregnant uterus
.