## Slide 1
Lab -5-
DRYING

## Slide 2: Drying
Drying
Drying :- is the removal of liquid from material by application of heat.
It is accomplished by
Transfer of a liquid from a surface into an unsaturated vapor phase.

## Slide 3: Purposes of drying:
1- Unit of process in pharmaceutical manufacturing
(e.g. preparation of granules then dispense as capsules or tablets).
2- Reduce bulk and weight lower the cost of transportation and storage.
3- Aid in preservation of animal and vegetable drugs:
A- Minimizing mold and bacterial growth in moisture laden material
B- Facilitate comminution by increasing friability.

## Slide 4: Classification of solids on drying behavior
1- Granular or crystalline solids (water is held in shallow and open surface pores as well as in interstitial spaces between particles that are easily accessible to the surface).
2- Amorphous, fibrous or gelatinous solids (moisture is an integral part of the molecular structure as well as being physically entrapped in fine capillaries and small interior pores).
Ex: starch, insulin and aluminum hydroxide.
Ex: calcium sulfate, zinc oxide, magnesium oxide
Note: Amorphous solids are difficult to dry than granular or crystalline solids.

## Slide 5: Classification of dryers
1- Static-bed dryers- systems
A- Tray and truck dryers
B- Tunnel and conveyor dryer
C-Oven
2- Moving-bed dryers-systems
A. Turbo-tray dryer
B. Pan dryer
3- Fluidized - bed dryers systems
4- Pneumatic dryers system
5- Specialized drying methods
A- Freeze dryer
B- Microwave drying

## Slide 6: 1- Static-bed dryers- systems
A- Tray and truck dryers: it consist from cabinet in which the material dried is spread on tiers of trays .

## Slide 7: 1- Static-bed dryers- systems
B- Tunnel and conveyor dryer: an adaptation of truck dryer for continuous drying.

## Slide 8: 1- Static-bed dryers- systems
C- Oven: including autoclave and dry oven

## Slide 9: 2- Moving-bed dryers-systems
The drying particles are partially separated so that they flow over each other.
A. Turbo-tray dryer
B. Pan dryer

## Slide 10: 3- Fluidized - bed dryers systems
Solid particles are partially suspended in upward moving gas steam.

## Slide 11: 4- Pneumatic dryers system
Drying particles are entrained and conveyed in a high velocity gas stream.

## Slide 12: 5- specialized drying methods
A- Freeze dryer

## Slide 13: 5- specialized drying methods
B- Microwave drying:- here instead of applying heat externally to material, energy in form of microwaves is converted into internal heat by interaction with material itself

## Slide 14: Solids drying
The moisture in a solid can be expressed on a wet-weight or dry-weight basis.
Wet-weight basis: loss on drying
%LOD = wt. of water in sample × 100
total wt. of wet sample
Dry-weight basis: moisture content
%MC = wt. of water in sample × 100
wt. of dry sample

## Slide 15: Example
If exactly 7 g of moist solid is brought to a constant dry weight of 5 g:
MC = x 100 = 40%
Whereas
LOD = x 100 = 28.57%