## Slide 1
  Unsaturated Systems – substitution patterns
    The substitution of aromatics and alkenes can also be discerned through the out-of-plane bending vibration region
    However, other peaks often are apparent in this region. These peaks should only be used for reinforcement of what is known or for hypothesizing as to the functional pattern.
Infrared Spectroscopy

## Slide 2
  Ethers – addition of the C-O-C asymmetric band and vinyl C-H bonds
    Show a strong band for the antisymmetric C-O-C stretch at 1050-1150 cm-1
    Otherwise, dominated by the hydrocarbon component of the rest of the molecule
Diisopropyl ether
Infrared Spectroscopy
(s)

## Slide 3
Alcohols
  Strong, broad O-H stretch from 3200-3400 cm-1
  Like ethers, C-O stretch from 1050-1260 cm-1
  Band position changes depending on the alcohols substitution: 1° 1075-1000; 2° 1075-1150; 3° 1100-1200; phenol 1180-1260
  The shape is due to the presence of hydrogen bonding
1-butanol
Infrared Spectroscopy
(m– s)
br
(s)

## Slide 4
  Amines - Primary
    Shows the –N-H stretch for NH2 as a doublet between 3200-3500 cm-1 (symmetric and anti-symmetric modes)
    -NH2 has deformation band from 1590-1650 cm-1
    Additionally there is a “wag” band at 780-820 cm-1 that is not diagnostic
2-aminopentane
Infrared Spectroscopy
(w)
(w)

## Slide 5
  Amines – Secondary
    N-H band for R2N-H occurs at 3200-3500 cm-1 as a single sharp peak weaker than –O-H
    Tertiary amines (R3N) have no N-H bond and will not have a band in this region
pyrrolidine
Infrared Spectroscopy
(w – m)

## Slide 6
Infrared Spectroscopy
  Pause and Review
    Inspect the bonds to H region (2700 – 4000 cm-1)
    Peaks from 2850-3000 are simply sp3 C-H in most organic molecules
    Above 3000 cm-1 Learn shapes, not wavenumbers!:
Broad U-shape peak
-O—H bond
V-shape peak
-N—H bond for 2o amine (R2N—H)
Sharp spike
-C≡C—H bond
W-shape peak
-N—H bond for 1o amine (RNH2)
3000 cm-1
Small peak shouldered just above 3000 cm-1 C=C—H or Ph—H

## Slide 7
  Aldehydes
    C=O (carbonyl) stretch from 1720-1740 cm-1
    Band is sensitive to conjugation, as are all carbonyls (upcoming slide)
    A highly unique sp2 C-H stretch appears as a doublet, 2720 & 2820 cm-1 called a “Fermi doublet”
Cyclohexyl carboxaldehyde
Infrared Spectroscopy
(w-m)
(s)

## Slide 8
  Ketones
    Simplest of the carbonyl compounds as far as IR spectrum – carbonyl only
    C=O stretch occurs at 1705-1725 cm-1
3-methyl-2-pentanone
Infrared Spectroscopy
(s)

## Slide 9
  Esters
    C=O stretch at 1735-1750 cm-1
    Strong band for C-O at a higher frequency than ethers or alcohols at 1150-1250 cm-1
Infrared Spectroscopy
Ethyl pivalate
(s)
(s)

## Slide 10
  Carboxylic Acids:
    Gives the messiest of IR spectra
    C=O band occurs between 1700-1725 cm-1
    The highly dissociated O-H bond has a broad band from 2400-3500 cm-1 covering up to half the IR spectrum in some cases
4-phenylbutyric acid
Infrared Spectroscopy
(w – m)
br
(s)
(s)

## Slide 11
  Acid anhydrides
    Coupling of the anhydride though the ether oxygen splits the carbonyl band into two with a separation of 70 cm-1
    Bands are at 1740-1770 cm-1 and 1810-1840 cm-1
    Mixed mode C-O stretch at 1000-1100 cm-1
Propionic anhydride
Infrared Spectroscopy
(s)
(s)

## Slide 12
  Acid halides
    Clefted band at 1770-1820 cm-1 for C=O
    Bonds to halogens, due to their size (see Hooke’s Law derivation) occur at low frequencies, only Cl is light enough to have a band on IR, C-Cl is at 600-800 cm-1
Propionyl chloride
Infrared Spectroscopy
(s)
(s)

## Slide 13
  Amides
    Display features of amines and carbonyl compounds
    C=O stretch at 1640-1680 cm-1
    If the amide is primary (-NH2) the N-H stretch occurs from 3200-3500 cm-1 as a doublet
    If the amide is secondary (-NHR) the N-H stretch occurs at 3200-3500 cm-1 as a sharp singlet
pivalamide
Infrared Spectroscopy
(m – s)
(s)

## Slide 14
  Nitro group (-NO2)
    Proper Lewis structure gives a bond order of 1.5 from nitrogen to each oxygen
    Two bands are seen (symmetric and asymmetric) at 1300-1380 cm-1 and 1500-1570 cm-1
    This group is a strong resonance withdrawing group and is itself vulnerable to resonance effects
2-nitropropane
Infrared Spectroscopy
(s)
(s)

## Slide 15
  Nitriles (the cyano- or –C≡N group)
    Principle group is the carbon nitrogen triple bond at 2100-2280 cm-1
    This peak is usually much more intense than that of the alkyne due to the electronegativity difference between carbon and nitrogen
propionitrile
Infrared Spectroscopy
(s)

## Slide 16
  Effects on IR bands
    Conjugation – by resonance, conjugation lowers the energy of a double or triple bond. The effect of this is readily observed in the IR spectrum:
      Conjugation will lower the observed IR band for a carbonyl from 20-40 cm-1 provided conjugation gives a strong resonance contributor
      Inductive effects are usually small, unless coupled with a resonance contributor (note –CH3 and –Cl above)
Infrared Spectroscopy

## Slide 17
  Effects on IR bands
    Steric effects – usually not important in IR spectroscopy, unless they reduce the strength of a bond (usually p) by interfering with proper orbital overlap:
      Here the methyl group in the structure at the right causes the carbonyl group to be slightly out of plane, interfering with resonance
    Strain effects – changes in bond angle forced by the constraints of a ring will cause a slight change in hybridization, and therefore, bond strength
      As bond angle decreases, carbon becomes more electronegative, as well as less sp2 hybridized (bond angle < 120°)
Infrared Spectroscopy

## Slide 18
  Effects on IR bands
    Hydrogen bonding
      Hydrogen bonding causes a broadening in the band due to the creation of a continuum of bond energies associated with it
      In the solution phase these effects are readily apparent; in the gas phase where these effects disappear or in lieu of steric effects, the band appears as sharp as all other IR bands:
      Gas phase spectrum of
      1-butanol
      Steric hindrance to H-bonding
      in a di-tert-butylphenol
      H-bonding can interact with other functional groups to lower frequencies
Infrared Spectroscopy