## Slide 1
Since the partitioning behavior is dependent on temperature, the separation column is usually contained in a thermostat-controlled oven.
Separating components with a wide range of boiling points is accomplished by starting at a low oven temperature and increasing the temperature over time to elute the high-boiling point components.

## Slide 2
A gas chromatography oven, open to show a capillary column

## Slide 3
  The mobile phase (carrier gas) should be chemically inert, dry, and free from O2 (helium, argon, nitrogen and hydrogen).
  The carrier gas should be of high purity; impurities in the carrier gas such as water vapour, air and trace gaseous hydrocarbons can cause reactions with sample and cause column deterioration and affect detector performance.
  The gas supply is associated with pressure regulator and flow controller.
Gas Supply
Gas
supply
Pressure
regulator
Flow
controller

## Slide 4
Sample Injection System
Flow meter
Gas
supply
Pressure
regulator
Flow
controller
Septum
Detector
Oven
Column
Injector
Recorder

GC
chart
Samples GC must be volatile.
Samples which are non volatile are converted into a volatile derivative.
Preparation of the Sample :
GC Column
Most GC columns are made from high-purity fused silica capillary, the inner wall of the capillary coated with the stationary phase.
GC columns vary in length from less than 2 m to 50 m or more.
In order to fit into the column oven, they are usually formed as coils.
The control of column’s temperature is critical to attain a good separation in GC, thus the column is located inside a thermostated oven to control the temperature.

## Slide 5
GC Detectors
Thermal conductivity detector (TCD)
Flame ionization detector (FID)
Nitrogen phosphorous detectors (NPD)

## Slide 6
Food Analysis
Analysis of foods is concerned with confirming the presence
and determination the quantities of the analytes (lipids,
proteins, carbohydrates, preservatives, flavors, colorants,
and also vitamins, steroids, and pesticide residues).
Drug Analysis
GC is widely applied to identification of the active components, possible impurities as well as the metabolites.
GC Applications:

## Slide 7
Forensic Analysis
In forensic cases, very little sample is available, and the
concentration of the sample components may be very low.
GC is a useful due to its high sensitivity and separation efficiency.
Environmental Analysis
The environmental contaminants; e.g. (DDT) is present in the environment at very low concentrations and are found among many of other compounds. GC, with its high sensitivity and high separating power, is mostly used in the analysis of environmental samples.

## Slide 8: Comparison of HPLC and GC
Sample Volatility
Sample Polarity
HPLC
No volatility requirement
Sample must be soluble in mobile phase
GC
Sample must be volatile
HPLC
GC
Separates both polar and non polar compounds
Samples are nonpolar and polar

## Slide 9: Comparison of HPLC and GC
Sample Preparation
Sample Size
HPLC
Sample must be filtered
Sample should be in same solvent as mobile phase
GC
Solvent must be volatile and generally lower boiling than analytes
HPLC
GC
Sample size based upon column.
Typically 1 - 5 L

## Slide 10: Comparison of HPLC and GC
Separation Mechanism
Detectors
HPLC
Both stationary phase and mobile phase take part
GC
Mobile phase is a sample carrier only
HPLC
GC
Most common UV-Vis
Wide range of non- destructive detectors
3-dimensional detectors
Most common FID, universal to organic compounds

## Slide 11
Thank you