## Slide 1: Characteristic Group Vibrations of Organic Molecules II

## Slide 3
Aromatic Hydrocarbons
Aromatic (C-H) stretching (3130-3030) cm-1
Aromatic (C-H) bending (900-650)
(1225-950) cm-1
Aromatic (C=C-C ) (1615-1580)
(1510-1450) cm-1
Monosubstitution (710-690) cm-1
Disubstitution (ortho) (770-730) cm-1
(meta) (810-750) (900-860) cm-1
(para) (860-800) cm-1
Aromatic ring (1600-1500) cm-1
o
o
m
m
p

## Slide 4
Aromatic Hydrocarbons
Monosubstitution
(710-690) cm-1
Aromatic (C-H ) stretching
(3130-3030) cm-1
Aromatic (C=C-C )
(1510-1450) cm-1
CH3
Monosubstituted aromatic ring

## Slide 5
Disubstituted aromatic ring (para)
CH3
O-H
(C-H) stretching
1650-1400 cm-1
(C=C) in-plane

## Slide 6
The combination and overtone bands in 2000-1650 cm-1 region are also characteristics of aromatic rings. Moreover, they are very weak and are observed only in the case of concentrated solutions of highly symmetric benzene derivatives.

## Slide 7
Alcohols and Phenols
The (C-O) and (O-H) absorption bands can be recognised from 3700 to 3400 cm-1
The presence of (N-H) or moisture causes similar results.
The exact position and shape of this band depends largely on the degree of H-bonding.
A strong and sharp peak in the region as higher 3700 cm-1 in gaseous or extremely dilute solutions represents unbounded or free OH group(s).

## Slide 8
Alcohols and Phenols
Alcohols and phenols in condensed phases (bulk liquid, KBr discs, concentrated solution etc.) are strongly hydrogen bonded, usually in the form of dynamic polymeric association; dimmers, trimers, tetramers etc., and cause broadened bands at lower frequencies.
H-bonding involves a lengthening of the original (O-H) bond. This bond is consequently weakened, force constant is reduced and so the stretching frequency is lowered.
(C-O) stretching (1250-1000) cm-1
(C-O) with (C-C) stretching mode
~1050 cm-1
~1100 cm-1
~1150 cm-1
These two bands can differentiate the types of alcohols and phenols

## Slide 9
Enols and Chelates
Since these bonds are not easily broken on dilution by an inert solvent, free (O-H) may not be seen at low concentrations.
In structures, such as 2,6-di -t-butylphenol, in which steric hindrance prevents hydrogen bonding, no bounded O-H band is observed, not even in spectra of neat samples.
O-H stretching 2880 cm-1
NO bounded O-H

## Slide 10
Ethers and Epoxides
Asymmetric (C-O-C) stretching 1150-1000 cm-1
But a band in this region is also observed in other oxy compounds like alcohols, aldehydes, ketones, and acids etc. Therefore, we consider the possibility that a compound is ether or an epoxide only if the unknown oxy compound shows no absorption bands in (O-H) (3750-3000 cm-1) or carbonyl (1850-1550 cm-1) regions. ((How can you recognize ether from other carbonyl groups?))
The conjugation of ether with (C=C) bond or phenyl ring shifts the (C-O-C) symmetric stretching to ~1250 cm-1. The resonance increases the bond order from single to partial double bond and so higher the force constant and higher the absorption frequency.

## Slide 11
Carbonyl compounds
The absorption peak for (C=O) stretching in the region 1870 to 1600 cm-1 is perhaps the easiest band to recognize in IR spectrum and is extremely useful in analysis of carbonyl compounds.
The changes in (C=O) stretching frequency in various carbonyl compounds can be explained by considering:
Electronic and mass effects of neighboring substituents
Resonance effects ( both C=C and heteroatom lone pair)
Hydrogen bonding (inter and intramolecular)
Ring strain etc.
It is customary to refer to the absorption frequency of a saturated aliphatic ketone at 1715 cm-1

## Slide 12
a. Aldehydes and Ketones
Aliphatic aldehydes show strong (C=O) stretching in the region of 1740 – 1725 cm-1.
The higher (C-H) stretching band (2860-2800 cm-1) of aldehyde is often buried under aliphatic C-H band. But the lower C-H band at 2760-2700 cm-1 is usually used to distinguish aldehydes from ketones. The C-H bending vibrations appear between 945-780 cm-1.
The conjugation of an aldehyde to a (C=C) or a phenyl group lowers (C=O) stretching by ~ 30 cm-1.
This effect is seen in benzaldehyde in which aryl group is attached directly to the carbonyl group and shifts (C=O) stretch to 1701 cm-1.

## Slide 13
a. Aldehydes and Ketones
1720-1700 cm-1

## Slide 14
a. Aldehydes and Ketones
In case of cyclic ketones, the coupling between (C=O) stretching and C(=O)-C single bond causes increase in C=O stretching frequency as the C-C(=O) angle decreases.

## Slide 15
b. Carboxylic Acids, Esters and Carboxylates
In case of carboxylic acids, the appearance of strong (C=O) stretching along with broad hydroxyl peak centered at ~ 3000 cm-1 in an IR spectrum certainly shows the presence of carboxylic acid. In addition a medium intensity (C=O) stretch appears between 1320 – 1260 cm-1. In dilute solutions, the carboxylic acids attain monomeric structures and the inductive effect of oxygen shifts the (C=O) absorption band to higher values 1760 – 1730 cm-1 than observed in ketones (1710 cm-1).
~1720 cm-1
3400-2500 cm-1

## Slide 16
b. Carboxylic Acids, Esters and Carboxylates
In case of α,β-unsaturated or aryl carboxylic acids esters, the esters of due to conjugation absorb at lower frequency.
1750-1730 cm-1
1300-1000 cm-1
If in an ester, (C-O) oxygen bears electron-withdrawing group like vinyl, Ph etc., then the (C=O) stretching is shifted to higher values (~1770 cm-1) This increases the electron-withdrawing ability of oxygen causing increase in carbonyl double bond character.
In cyclic esters (lactones) (C=O) stretching is shifted to higher frequency with decreasing ring size. Because of ring strain.
In salts of carboxylic acids, expected due to partial (C=O) bond character, the C=O stretching frequency is shifted to lower frequencies at ~ 1600 cm-1.

## Slide 17
c. Acid Chlorides and Anhydrides
Both carboxylic acid halides and anhydrides show strong (C=O) absorptions at frequencies > 1800 cm-1 , and are easily differentiated form other carbonyl compounds.
The acid anhydrides show two absorption bands in carbonyl region at 1820 cm-1 due to symmetric and at 1760 cm-1 due to asymmetric stretching vibrations.
In case of anhydrides of conjugated carboxylic acids, the frequencies due to these bands are shifted to 1775 and 1720 cm-1.

## Slide 18
c. Acid Chlorides and Anhydrides
The effect of conjugation is clearly visible in IR spectrum of benzoyl anhydride. The strong and broad (C-O) stretching vibrations appear in the region 1300 – 900 cm-1.
In case of acid chlorides, the (C=O) stretching frequencies appear at 1810-1790 cm-1 which is attributed to high electronegativity of chlorine

## Slide 19
d. Amides
In case of amides strong resonance participation of lone pair of electrons by amide nitrogen weakens the carbonyl bond, Consequently:
The (C=O) stretching band in IR spectra of amide is called amide I band.
In primary and secondary amides, (N-H) deformation band appears in the region 1655 - 1595 cm-1 and is called amide II band.
In the solid or pure liquid state, primary amides, which are highly hydrogen bonded, exhibit two N-H stretching bands, one at 3550 cm-1 due to N-H asymmetric stretching and other at 3180 cm-1 due to N-H symmetric stretching.
In dilute solutions, due to lowering in degree of hydrogen bonding, the absorption bands shift to higher frequencies at 3500 and 3400 cm-1 , respectively. The secondary amides show only one (N-H) band at ~ 3300 cm-1.
1680-1630 cm-1
20-50 cm-1 lower than ketones
(C=O) amide < (C=O) ketone