## Slide 1
Biopharmaceuitcs lab 6
In vitro dissolution study of per – oral tablet

## Slide 2
Introduction :
Dissolution is a process of going into
solution form .
A basic principle of drug absorption is that absorption takes place only after a drug is in solution .this means that drug given orally in solid dosage form must dissolve in GIT fluid before absorption occurs

## Slide 3: The following process occurs before absorption of solid dosage forms
Notes :
Pero- oral means taken orally
Oral means work on oral cavity

## Slide 4
When drug is slightly soluble the rate limiting factor for absorption is dissolution
Dissolution and Absorption
While for highly soluble drug the rate limiting factor is absorption

## Slide 5: Factors affecting dissolution rate
Agitation intensity
Drug solubility
Surface area exposed to dissolution medium

## Slide 6
Method :
By using dissolution apparatus (karl kolb)
(apparatus 2 paddle type )
The conditions of the experiment are made so that they simulate body conditions .
A temperature 37 º C and a rotation speed of 50 r.p.m
The dissolution medium is artificial gastric juice or artificial intestinal juice .

## Slide 7
Dissolution testing is a key quality control test
• Dissolution tests can be conducted in simple buffer solutions or in more bio-relevant dissolution media
• Dissolution tests are normally performed under sink conditions
• There are four types of compendial dissolution apparatus: the basket apparatus (USP I), the paddle apparatus(USPII) , the reciprocating cylinder and the flow-through cell
•A dissolution test is said to be performed under sink conditions if the concentration of the drug in the bulk of the dissolution medium does not exceed 10% of the solubility of the drug.

## Slide 8
Under sink conditions, the concentration gradient between the diffusion layer surrounding the solid drug particles and the concentration in the dissolution medium is assumed to be constant

## Slide 11: Sampling point USP/NF – midway from top of basket or paddle to top of fluid and no closer than 1 cm to side of flask BP – halfway between basket and side at middle of basket

## Slide 12: Procedure ( Dissolution study of nitrofurantoin tablets)
Fill the jars with 1 L of dissolution fluid (artificial gastric juice)
Put the jars in a thermostatically controlled water bath at 37 (switch water bath on)
Place 1 tablet of nitrofurantoin in the basket of apparatus, and start the instrument immediately
Set the speed on 50 r.p.m
With draw 5 ml each 10 min for 1.5 hr

## Slide 13: Notes
stop apparatus for withdrawal.
Substitute for the volume withdrawn each time interval using a fresh (artificial gastric juice) previously maintained at 37º C
After withdrawal and replacement start instrument again
Analyze samples of nitrofurantoin by reading the absorbance on a spectronic -20 at 369 nm ~370 nm immediately because nitrofurantoin solution discolored by exposure to light
Use the following stright line equation to obtain the concentartion of y= c+bx , y= AB, X= conc.(mg/100ml), c=0.01, b=0.4

## Slide 14
Collection time (min) | Ab | Conc.(mg/ml) | Percent drug release
10 |  |  | 
20 |  |  | 
30 |  |  | 
40 |  |  | 
50 |  |  | 
60 |  |  | 
75 |  |  | 
90 |  |  | 

## Slide 15
To obtain percent drug release:
Con.(mg/ml)X vol. of dissolution media =mg amount of drug released into the dissolution media
% of drug released = amount of drug release /amount of drug in the tablet *100
Plot the following graphs :
1. drug release % versus time in (min)
2. log % drug released versus time in (min)
Find dissolution rate K from
the slope
K= slope * 2.303
Note : amount of drug is
equal to 100 mg in each tab

## Slide 16: Working example using EXCEL SHEET

## Slide 17
Switch the sheet direction so that the first column is on right side

## Slide 18
Note units of x are given in u/ml in this example

## Slide 19
After completing calculation press ENTER
Then DRAG

## Slide 23
To add titles

## Slide 25
Thank you