## Slide 1
LAB.2
Direct compression
Fifth stage
Industrial pharmacy
2024-2025

## Slide 2: Tablet production methods
There Are Three Methods Of Tablet Manufacture Designed To Confer These Essential Attributes To A Tablet Formulation.
Wet Granulation And Direct Compression Are The Most Important, With
Dry Granulation Used In Some Circumstances
Regardless Whether Tablets Are Made By Direct Compression Or Granulation, The First Step Which Is, Milling And Mixing, Is The Same; Subsequent Step Differ.

## Slide 3: Direct compression
direct compression is the easiest and most cost-effective process for tablet manufacturing, because it only involves blending and compression.
consists of compressing the substances together with any substance of physical property enable to compress directly with good flowability.
a crystalline structure, is more easily to compress than amorphous form because of the creation of certain cohesive bonds between crystals due to the pressure of compression, whereas in amorphous form it will not.
addition of a disintegrant to the formulation will aid to avoid the major problems in disintegration like (long time dissolution and melting). Disintegration of conventional compressed tablet must occur within 15 minutes.

## Slide 4
Simplely it includes blending the API and excipients followed by compression

## Slide 5
not all materials can be easily or directly compressed:
  most materials having weak intermolecular attracting forces.
  large doses drugs do not lend themselves to this technique due to:
    need of additives in a ratio of 1:1 for e.g. active constituent 500mg and diluent 500mg so will form (large tab., costly, difficult to swallow and not accepted by patients).
  small doses drugs can’t be compressed directly like digoxin because there may be not sure to distribute uniformly.
  NOTE: Materials with improper functionalities could lead to serious problems , such as sticking; content non-uniformity and capping

## Slide 6: Ideal direct compression excipients:
Flowability
Stable, inert, compatible
Compressibility
Particle size should be of high range, to meet the particle size of the drug (be close to it) Otherwise segregation (demixing) will occur leading to lack of content uniformity
Low cost
Provide high pressure-hardness profile.
It is important to note that many excipients can possess multi-functionality, which is dependent upon the concentration at which they are employed. For example, microcrystalline cellulose can be used as an anti-adherent (5–20%), a disintegrant (5–15%) and as a diluent (20–90%).

## Slide 7: Advantages of Direct Compression:
• Requires fewer unit operations compared with wet granulation (shorter processing time and lower energy consumption)
• fewer stability issues for actives that are sensitive to heat or moisture
• For certain compounds, faster dissolution rates may be generated from tablets prepared by direct compression compared with wet granulation; for example, norfloxacin
• fewer excipients may be needed in a direct compression formula

## Slide 8: Disadvantages of Direct Compression
• Issues with segregation – these can be reduced by matching the particle size and density of the active drug substance with excipients
• Reactions of excipients with the drug like reaction of spray dry lactose with amine resulting in yellowish discoloration while the original color is brown (incompatibility).
• In general, the drug content is limited to approximately 30% or approximately 50 mg.
• May not be applicable for materials possessing a low bulk density because after compression the tablets produced may be too thin.
• Not suited for poorly flowing drug compounds.
• Static charges may develop on the drug particles or excipients during mixing, which may lead to agglomeration of particles producing poor mixing.

## Slide 9: Experiment Part
Aim of experiment :
Preparation of aspirin tablets by direct compression
Preformulation test:
Organoleptic properties
  (crystalline –tubular or needle shape)
  Bitter or slightly acidic taste
  Odorless or have odor due to formation of acetic acid and S.A. in the presence of moisture.

## Slide 10
Solubility
  Slightly soluble in water (1:300), highly soluble in organic solvent (1:5-7 alcohol, 2:10-17 ether, 1:17 chloroform).
  Partition coefficient High (high solubility in lipids) and thus having good absorption in GIT wall so it is highly absorbed from stomach but also having good absorption from small intestine due to large surface area.
Stability
  (unstable in water) due to decomposition (hydrolysis) so it dissolves in aq. Solution of carbonate and alkali hydroxyl with decomposition

## Slide 11: Formula
Aspirin 75mg (api)
Starch 10mg (disintegrant)
Lactose 40mg (diluent)
Mg stearate 2mg (lubricant)
Mix all ingredients together after weighing (aspirin, disintegrant , diluent) for 15 minutes
Then add the lubricant and mix for not more than 5 minutes
Directly compress
lubricant is added at last step . Why?

## Slide 12
Thank you