## Slide 1: Computer Science Networks & the effects of using them

## Slide 2: What is a Network?
Definition: A system of two or more nodes (devices) interconnected via a transmission medium (guided or unguided) to share resources and data.
Essential elements of any network:
  End devices: Computers, printers, smartphones.
  Intermediate devices: Switches, routers, access points.
  Media: Copper wires, fiber optics, electromagnetic waves.
Benefits (economic & operational):
  Cost reduction (share printers/software).
  Increased reliability (backups).
  Scalability.
  Communication and collaboration.

## Slide 3: Network Interface Card (NIC)
Full name: Network Interface Card (or network adapter).
Function: Converts data from parallel (inside computer) to serial (on the medium) and vice versa.

## Slide 4: Network Interface Card (NIC)
Internal components of a NIC:
  Buffer memory.
  Microcontroller/processor.
  Connector (RJ45 for copper, antenna for wireless).
  Permanent memory storing the MAC address (burned-in).
Types: Wired (Ethernet), wireless (Wi-Fi), onboard (integrated), or external (USB).

## Slide 5: MAC Address
Mathematical & logical definition: A globally unique identifier of 48 bits (6 bytes), used at the Data Link Layer (Layer 2 of OSI).
Format: 12 hexadecimal digits, grouped as 6 pairs separated by colons or hyphens.
Example : 00-1C-B3-4F-25-FF
Structure:
  First 24 bits (3 bytes): OUI (Organizationally Unique Identifier) assigned by IEEE to manufacturers (e.g., Apple, Intel).
  Last 24 bits (3 bytes): Unique serial number assigned by the manufacturer.

## Slide 6: MAC Address
Properties:
  Static: Does not change unless the NIC is replaced (though MAC spoofing is possible).
  Physical: Used only within the local network (does not cross a router).
Importance: Essential for switching – switches use MAC address tables.

## Slide 8: IP Address – IPv4 vs IPv6
Definition: A logical (non-permanent) identifier used at the Network Layer (Layer 3) to locate a device on a wide network (e.g., the internet).
IPv4 (32 bits):
Format: Four decimal numbers (0–255) separated by dots. Example: 192.168.1.1
Problem: Address exhaustion (only ~4.3 billion addresses).

## Slide 9: IPv6 (128 bits)
Format: Eight groups of four hexadecimal digits separated by colons. Example: 2001:0db8:85a3:0000:0000:8a2e:0370:7334
Features: Vast address space (~340 undecillion), built-in security (IPsec), autoconfiguration (SLAAC)
Stateless Address Autoconfiguration
Internet Protocol Security

## Slide 10: Key difference between MAC and IP:
Key difference between MAC and IP:
  MAC = identity (like a national ID number).
  IP = location address (like a postal address – changes when you move).

## Slide 11: Data Packets
Why split data into packets?
  Efficient use of bandwidth.
  Avoids line monopolization (multiplexing).
  Only corrupted packets are retransmitted.

## Slide 12: Data Packets
Packet structure:
  Header:
    Source IP address
    Destination IP address
    Sequence number (for reordering)
    Identification number (ties packets to original message)
    Time To Live (TTL) – prevents infinite looping
    Protocol type (TCP/UDP)
  Payload: The actual data fragment (part of a file, web page, etc.).
  Trailer (optional): Error-checking data (e.g., CRC).