## Slide 1: Structural Design of Highway
Third Stage
Lecture 9
Lecture. Dr. Rana Amir Yousif
Highway and Transportation Engineering
Al-Mustansiriyah University
2017

## Slide 2
References:
1. Nicholas J. Garber and Lester A. Hoel.”Traffic and Highway Engineering”, Fourth Edition.
2.Yoder; E. J. and M. W. Witczak, “Principles of Pavement Design”, A Wiley- Interscience Publication, John Wiley & Sons Inc., U.S.A., 1975.
3. Yaug H. Huang, “Pavement Analysis and Design”, Prentic Hall Inc., U.S.A., 1993.
4.“AASHTO Guide for Design of Pavement Structures 1993”, AASHTO, American Association of State Highway and Transportation Officials, U.S.A., 1993.
5. Oglesby Clarkson H., “Highway Engineering”, John Wiley & Sons Inc., U.S.A.,1975.

## Slide 3: Design Traffic Loading and contact area K= MR/19.4

## Slide 4
From zero up to pavement depth of d/2 , the dual wheel ( 4 ton) produce the same deflection on a single wheel load (2 ton)
For depth of (2S) or greater, over lapped stress of dual wheels (4 ton) shall cause equivalent deflection of single wheel load with (4 ton)

## Slide 5
Example 1 .1 :
Draw the most realistic contact area for an 18-kip (80-kN) single-axle load with a tire pressure of 80 psi (552 kPa) . What are the other configurations of contact area that have been used for pavement design ?

## Slide 7: CHAPTER 11 Flexible Pavement Design
Climate Models
Temperature and moisture are significant climatic inputs for pavement design. The modulus of the HMA depends on pavement temperature; the moduli of the base, subbase, and subgrade vary appreciably with moisture content.
Heat Transfer Model
The heat transfer model was originally developed at the University of Illinois (Dempsey and Thompson, 1970) for evaluating frost action and temperature regime in multilayered pavement systems. The model applies the finite difference method to solve the following Fourier equation for one-dimensional heat flow:
Here, T is the temperature, t is the time, z is the depth below surface, and a is the thermal diffusivity, which is related to the thermal conductivity and heat capacity of the pavement materials. Given the initial temperature distribution and the two boundary conditions (at the pavement surface and at a depth H below the surface), Eq.11.1 can be solved.

## Slide 8
Moisture Equilibrium Model
The moisture equilibrium model in the CMS model (Dempsey et al., 1986) is based on the assumption that the subgrade cannot receive moisture by infiltration through the pavement. Any rainwater will drain out quickly through the drainage layer to the side ditch or longitudinal drain, so the only water in the subgrade is the capillary water caused by the water table. Because of the thermodynamic relationship between soil suction and moisture content, a simple way to determine the moisture content in a soil is to determine its suction, which is related to the pore water pressure.
Figure 11 .2 shows the suction–moisture curves for five different soils with varying clay contents, as indicated by the numerals in parentheses under each soil title. These curves were obtained in the laboratory by drying tests, in which different levels of vacuum or suction were applied to a wet soil specimen until the moisture was reduced to an equilibrium value. The suction is expressed in the pF scale, which is the logarithm of water tension in cm, as defined by Schofield (1935) . The corresponding values in terms of psi are shown on the left scale. It can be seen that suction increases as the moisture content decreases or the clay content increases. The increase in suction is due to the soil particles. In the CMS model, empirical relationships were used to define the suction—moisture curve based on the liquid limit, the plasticity index, and the saturated When there is no loading or overburden pressure, suction is equal to the negative pore pressure. When a load or overburden is applied to an unsaturated soil with given moisture content or suction, the suction or moisture content remains the same but the pore pressure becomes less negative. The relationship between suction and pore pressure can be expressed as:

## Slide 9
in which u is the pore pressure when soil is loaded ; S is the soil suction, which is a negative pressure ; p is the applied pressure (or overburden), which is always positive ; and a is the compressibility factor, varying from 0 for unsaturated, cohesionless soils to 1
for saturated soils . For unsaturated cohesive soils, a is related to the plasticity index P I
by (Black and Croney, 1957)
in which u is the pore pressure when soil is loaded ; S is the soil suction, which is a negative pressure ; p is the applied pressure (or overburden), which is always positive ; and a is the compressibility factor, varying from 0 for unsaturated, cohesionless soils to 1
for saturated soils . For unsaturated cohesive soils, a is related to the plasticity index P I
by (Black and Croney, 1957)
The pore pressure in a soil depends solely on its distance above the ground-water
table:

## Slide 10
Here, z is the distance above the water table, and yw is the unit weight of water. This simple fact can be explained by considering soils as a bundle of capillary tubes with varying sizes. Water will rise in each of these capillary tubes to an elevation that depends on the size of the tube. At any distance z above the water table, a large number of menisci will form at the air—water interfaces, causing a tension at each elevation corresponding to the height of capillary rise. Combining Eqs. 11 .2 and 11 .4 yield s
The procedures for determining the equilibrium moisture content at any point in a pavement system can be summarized as follows:
1. Determine the distance z from the point to the water table.
2. Determine the loading or overburden pressure p.
3. Determine the compressibility factor a from Eq .11.3 .
4. Determine the suction S from Eq .11.5 .
5. Determine the moisture content from the suction–moisture curve.

## Slide 12
Example 11.1:
Figure 11 .3 shows an 8-in . (203-mm) full-depth asphalt pavement on a subgrade composed of two different materials. The top 16 in . (406 mm) of subgrade is a Culham sand ; below it is a Norton clay with a PI of 18 . The relationship between the suction and moisture content of these two soils is shown in Figure 11.2 . The water table is located 12 in . (305 mm) below the top of the clay. The unit weight y of each material is shown in the figure . Predict the moisture contents at point A on top of the clay, point B at the bottom of the sand layer, and point C on top of the sand layer .

## Slide 13
Solution : At point A, the overburden pressure p = (8 × 145 + 16 × 120)/12 = 256 .7 psf.
From Eq. 11 .3, a = 0 .03 x 18 = 0 .54. From Eq. 11 .5, S = -1 × 62 .4 – 0 .54 × 256 .7 =
-201.0 psf = -1 .40 psi. From Figure 11 .2, the moisture content is 38%.
At point B, a = 0 and, from Eq. 11 .5, S = -62.4 psf = -0 .43 psi. From Figure 11 .2, the moisture content is 21 % .
At point C, from Eq. 11 .5, S = –(12 + 16) × 62.4/12 = -145.6 psf = 1 .01 psi . From
Figure 11 .2, the moisture content is 19 .5%.

## Slide 14
Structural Models
Finite Element Models
Elastic Layer Programs