## Slide 1: High Performance Computing

## Slide 2: Recap
SMP
Clustering

## Slide 3: Today’s topics
NUMA (Non-Uniform Memory Access)
Cache Coherence

## Slide 4: Nonuniform Memory Access (NUMA)
UMA: Uniform memory access
  All processors have access to all parts of memory
    Using load & store
  Access time to all regions of memory is the same
  Access time to memory for different processors same
  As used by SMP
Nonuniform memory access
  All processors have access to all parts of memory
    Using load & store
  Access time of processor differs depending on region of memory
  Different processors access different regions of memory at different speeds
Cache coherent NUMA
  Cache coherence is maintained among the caches of the various processors
  Significantly different from SMP and clusters

## Slide 5: Motivation
SMP has practical limit to number of processors
  Bus traffic limits to between 16 and 64 processors
In clusters each node has own memory
  Apps do not see large global memory
  Coherence maintained by software not hardware
NUMA retains SMP flavour while giving large scale multiprocessing
  e.g. Silicon Graphics Origin NUMA 1024 MIPS R10000 processors
Objective is to maintain transparent system wide memory while permitting multiprocessor nodes, each with own bus or internal interconnection system

## Slide 6: CC-NUMA Organization

## Slide 7: CC-NUMA Operation
Each processor has own L1 and L2 cache
Each node has own main memory
Nodes connected by some networking facility
Each processor sees single addressable memory space
Memory request order:
  L1 cache (local to processor)
  L2 cache (local to processor)
  Main memory (local to node)
  Remote memory
    Delivered to requesting (local to processor) cache
Automatic and transparent

## Slide 8: Cache Coherence
Node 1 directory keeps note that node 2 has copy of data
If data modified in cache, this is broadcast to other nodes
Local directories monitor and purge local cache if necessary
Local directory monitors changes to local data in remote caches and marks memory invalid until writeback
Local directory forces writeback if memory location requested by another processor

## Slide 9: NUMA Pros & Cons
Effective performance at higher levels of parallelism than SMP
No major software changes
Performance can breakdown if too much access to remote memory
  Can be avoided by:
    L1 & L2 cache design reducing all memory access
      Need good temporal locality of software
    Good spatial locality of software
    Virtual memory management moving pages to nodes that are using them most
Not transparent
  Page allocation, process allocation and load balancing changes needed
Availability?

## Slide 10: Cache Coherence
In SMP or NUMA, multiple copies of cache
  Each copy may have a different value of data item
  Maintain Coherency
    How?

## Slide 11: Cache Coherence: Two Approaches
Write back: Update Main memory once cache is flushed.
Write through: Write is updated to cache as well as to the main memory.

## Slide 12: Implementations
Software Solutions:
  Compile time decision
  Conservative
  Inefficient cache utilization
Hardware Solutions:
  Runtime decision
  More effective

## Slide 13: Hardware based solution
Directory Protocol
Snoopy Protocol

## Slide 14: Directory
Centralized Controller
  Individual cache controller makes a request
    Centralized controller checks and issues command
  Updates information

## Slide 15: Directory
Write
  Processor requests exclusive writes
  Controller sends message
  Invalidates
Read
  Issues command to the processor
  Holding Processor
    Writes back to MM
    Read permitted

## Slide 16: Directory
Disadvantage
  Centralized Controller
  Bottleneck
Advantage
  Useful in large –scale system

## Slide 17: Snoopy Protocol
Update operation announced
All Cache controllers snoop
Bus architecture
  Careful
    Increased Bus Traffic

## Slide 18: Snoopy Protocol
Two approaches
  Write Invalidate
    One write
    Multiple readers
    Exclusive: Writer invalidates others entries
  Write Update
    Multiple writers
    All writes are updated

## Slide 19: Write Invalidate
The MESI Protocol : P4 processor
  Data cache: Two status bits, 4 states
    Modified
    Exclusive
    Shared
    Invalid
    See Table