## Slide 1: Route Location
01
Reference: Nicholas J. Garber, Lester A. Hoel, TRAFFIC AND HIGHWAY ENGINEERING, Fourth Edition
Ch. 14, page 691

## Slide 2: Principles of Highway Location
1. Office Study of Existing Information
Engineering, including topography, geology, climate, and traffic volumes
Social and demographic, including land use and zoning patterns
Environmental, including types of wildlife; location of recreational, historic, and archeological sites; and the possible effects of air, noise, and water pollution
Economic, including unit costs for construction and the trend of agricultural, commercial, and industrial activities

## Slide 3
2. Reconnaissance Survey
Terrain and soil conditions
Serviceability of route to industrial and population areas
Crossing of other transportation facilities, such as rivers, railroads, and highways
Directness of route

## Slide 4
3. Preliminary Location Survey
a. Economic Evaluation
Economic evaluation of each alternative route is carried out to determine the future effect of investing the resources necessary to construct the highway.
The evaluation methods described in Chapter 13 [Evaluating Transportation Alternatives] are used for this decision process. Factors usually taken into consideration include road user costs, construction costs, maintenance costs, road user benefits, and any disbenefits, which may include adverse impacts due to dislocation of families, businesses, and so forth. The results obtained from the economic evaluation of the feasible routes provide valuable information to the decision maker. For example, these results will provide information on the economic resources that will be gained or lost if a particular location is selected.
This information is also used to aid the policy maker in determining whether the highway should be built, and if so, what type of highway it should be.

## Slide 5
b. Environmental Evaluation
Federal legislation has been enacted that sets forth the requirements of the environmental evaluation required for different types of projects. In general, the requirements call for the submission of environmental impact statements for many projects.
These statements should include:
• A detailed description of alternatives
• The probable environmental impact, including the assessment of positive and negative effects
• An analysis of short-term impact as differentiated from long-term impact
• Any secondary effects, which may be in the form of changes in the patterns of social and economic activities
• Probable adverse environmental effects that cannot be avoided if the project is constructed
• Any irreversible and irretrievable resources that have been committed

## Slide 6
Final Location Survey
The final location survey is a detailed layout of the selected route. The horizontal and vertical alignments are determined, and the positions of structures and drainage channels are located. The method used is to set out the points of intersections (PI) of the straight portions of the highway and fit a suitable horizontal curve between these.
Detailed design of the vertical and horizontal alignments is then carried out to obtain both the deflection angles for horizontal curves and the cuts or fills for vertical curves and straight sections of the highway.

## Slide 7
Location of Highways in Urban Areas
Connection to Local Streets
When the location of an expressway or urban freeway is being planned, it is important that adequate thought be given to which local streets should connect with on- and offramps to the expressway or freeway. The main factor to consider is the existing travel pattern in the area. The location should enhance the flow of traffic on the local streets.
The location should provide for adequate sight distances at all ramps. Ramps should not be placed at intervals that will cause confusion or increase the crash potential on the freeway or expressway.

## Slide 8
Right-of-Way Acquisition
One factor that significantly affects the location of highways in urban areas is the cost of acquiring right of way. This cost is largely dependent on the predominant land use in the right of way of the proposed highway. Costs tend to be much higher in commercial areas, and landowners in these areas are often unwilling to give up their property for highway construction. Thus, freeways and expressways in urban areas have been placed on continuous elevated structures in order to avoid the acquisition of rights of way and the disruption of commercial and residential activities. This method of design has the advantage of minimal interference with existing land-use activities, but it is usually objected to by occupiers of adjacent land because of noise or for aesthetic reasons. The elevated structures are also very expensive to construct and therefore do not completely eliminate the problem of high costs.

## Slide 9
Coordination of the Highway System with Other Transportation Systems
Urban planners understand the importance of a balanced transportation system and strive toward providing a fully integrated system of highways and public transportation.
This integration should be taken into account during the location process of an urban highway. Several approaches have been considered, but the main objective is to provide new facilities that will increase the overall level of service of the transportation system in the urban area. In Washington, D.C., for example, park-and-ride facilities have been provided at transit stations to facilitate the use of the Metro system, and exclusive bus lanes have been used to reduce the travel time of express buses during the peak hour.
Principles of Bridge Location
The basic principle for locating highway bridges is that the highway location should determine the bridge location, not the reverse.

## Slide 10
Highway Survey Methods
Ground Surveys
Remote Sensing
Remote sensing is the measurement of distances and elevations by using devices located above the earth, such as airplanes or orbiting satellites using Global Positioning Satellite systems (GPS). The most commonly used remote-sensing method is photogrammetry, which utilizes aerial photography. Photogrammetry is the science of obtaining accurate and reliable information through measurements and interpretation of photographs, displaying this information in digital form and/or map form. This process is fast and economical for large projects but can be very expensive for small projects. The break-even size for which photogrammetry can be used varies between 30 and 100 acres, depending on the circumstances of the specific project. The successful use of the method depends on the type of terrain. Difficulties will arise when it is used for terrain with the following characteristics.
Areas of thick forest, such as tropical rain forests, that completely cover the ground surface
Areas that contain deep canyons or tall buildings, which may conceal the ground surface on the photographs
Areas that photograph as uniform shades, such as plains and some deserts

## Slide 11
Highway Earthwork and Final Plans
The final element in the location process is to establish the horizontal and vertical alignments of the highway project and to prepare highway plans and specifications for estimating project costs and preparation of bids by contractors.
Highway Grades and Terrain
One factor that significantly influences the selection of a highway location is the terrain of the land, which in turn affects the laying of the grade line. The primary factor that the designer considers on laying the grade line is the amount of earthwork that will be necessary for the selected grade line. One method to reduce the amount of earthwork is to set the grade line as closely as possible to the natural ground level.
This is not always possible, especially in undulating or hilly terrain. The least overall cost also may be obtained if the grade line is set such that there is a balance between the excavated volume and the volume of embankment. Another factor that should be considered in laying the grade line is the existence of fixed points, such as railway crossings, intersections with other highways, and in some cases existing bridges, which require that the grade be set to meet them. When the route traverses flat or swampy areas, the grade line must be set high enough above the water level to facilitate proper drainage and to provide adequate cover to the natural soil.

## Slide 12
Preparation of Highway Plans
Fig. 14.18