## Slide 1: 1CREEP
الجامعة المستنصرية
كلية الهندسة – قسم الهندسة الميكانيكية
مادة موا هندسية
د. ناظم مجبل فالح

## Slide 2: Introduction
Creep is the permanent elongation of a component under a static load maintained for a period of time.
It is a phenomena of metals and of certain nonmetallic materials eg thermoplastic and rubbers.
It can occur at any temperature.

## Slide 3
Example
    Lead - creeps under a constant tensile load at room temperature
    metals and their alloys – creep of any significance occur at elevated temp.
    aluminum alloy - 200°C
    refractory alloys - 1500°C
the mechanism of creep at elevated temp in metals is generally attributed to grain-boundary sliding

## Slide 4: Why creep is important?
Creep is especially important in high-temperature application eg;
    gas-turbine blades
    component in jet engines and rocket motors.
    high-pressure steam lines
    nuclear-fuel element
    tools and dies that subjected to high stresses at elevated temp. during hot-working operation- forging and extrusion