## Slide 1: Design of Stable Channels CH-4
Grass-Lined Channels

## Slide 2: Providing Channel Protection
For bare soil channels, allowable shear stress is small –
  Results in channels that are wide with shallow flows
If the channel can be protected from erosion, then allowable velocities can be increased – Vegetation!
Grass-lined channels are common in urban areas to transmit storm water
  Usually preferred to concrete lined channels
  Design is different because these channels cannot withstand lengthy inundation and wetness
Channel Roughness – Manning’s n becomes a strong function of U, Rh, and vegetation type (height)
  Experimental work has shown that Manning’s n can be related to URh

## Slide 3: Retardance Classes (SCS, 1969)

## Slide 4: Guide to Selection of Vegetal Retardance

## Slide 5: Manning’s n-URh Relationship

## Slide 6: Manning’s n-URh Relationship
Temple et al. (1987) developed the following approximation for the Manning’s n–URh relationships:
Retardance | I
A | 10.000
B | 7.643
C | 5.601
D | 4.436
E | 2.876

## Slide 7: Maximum Permissible Velocities
  Suggested by SCS based on channel slope and erodibility of soil

## Slide 8: Maximum Permissible Velocities

## Slide 9: Freeboard Requirement
Freeboard requirement (should be at least 30 cm):

## Slide 10: Design Procedure
Stage 1
  Assume an n value and determine value of URh
  The lower bound retardance of the channel is specified based on the type of grass
  Select maximum permissible velocity and compute the value of Rh
  Use Manning’s equation and the assumed value of n to compute a URh
  Repeat steps 1-4 until the values of URh agree
  Determine A from the design flow and maximum permissible velocity
  Determine the channel proportions for the calculated values of Rh and A

## Slide 11: Design Procedure
Stage 2
  Assume a depth of flow for the channel identified in Stage 1 of the design and compute A and Rh
  Compute the average velocity, U = Q/A
  Compute URh using steps 1 and 2
  Use the results of step 3 to determine n using the upper bound retardance
  Use the n from step 4, Rh from step 1, and the Manning equation to compute U
  Repeat steps 1 through 5 until values of U in steps 2 and 5 are approximately equal
  Add the appropriate freeboard

## Slide 12: Example
Design a triangular grass-lined channel to handle an intermittent flow of 0.7 m3/s. The channel is to be excavated in an easily erodible soil (d50 = 1 mm, j = 35o) on a longitudinal slope of 2%, and lined with Bermuda. During the early stages of the channel development, the height of the grass will be maintained at 4 cm; during the latter stages of development, the Bermuda will be at a height of 30 cm.