## Slide 1: Fluid Mechanics Lectures 2nd year/2nd semister/2018-2019/Al-Mustansiriyah unv./College of engineering/Highway &Transportation Dep.Lec.1

## Slide 2
. Example : Network pipeline (Hardy-Cross method):
Find floe rate for each pipe in network (fig.6)using Hardy-cross method, the length of AB, BD, CD,AC and BC are 2000 ft, 1500ft, 2000 ft, 1500 ft and 2500 ft respectively, all pipes have diameter of 6 in ,the friction factor for each pipe is 0.022?

## Slide 3
.
)
Pipe | Q ft3/s | V=Q/A | f | L | Hf=f*L/D*v2/2g | hf/Q
AB | -1.5 | 7.6 | 0.022 | 2000 | -78.9 | 52.6
BC | -0.25 | 1.3 | 0.022 | 2500 | -2.89 | 11.5
AC | +0.5 | 2.5 | 0.022 | 1500 | +6.4 | 12.8
∑ |  |  |  |  | -75.39 | 76.91
Loop 1
ΔQ =-hf1.85(hf/Q) = -(75.391.85( 76.91) = 0.5 ft3/s = 0.015 m3/s =15 L/s˃ 3 L/s
not. Ok

## Slide 4
Pipe | AB | BC | AC
Corrected flows | -1 | 0.25 | +1
Pipe | Q ft3/s | V=Q/A | f | L | Hf=f*L/D*v2/2g | hf/Q
BC | +0.25 | 1.3 | 0.022 | 2000 | +2.89 | 11.5
CD | +0.25 | 1.3 | 0.022 | 2000 | +2.31 | 9.24
BD | -0.25 | 1.3 | 0.022 | 1500 | -1.73 | 6.92
∑ |  |  |  |  | +3.47 | 27.66
Pipe | BC | CD | BD
Corrected flows | +0.25 | 0.25 | -0.25
not. Ok
Loop 2
ΔQ =-hf1.85(hf/Q) = -(3.47)1.85( 27.66) = 0.06 ft3/s = 0.002 m3/s = 2 L/s˂ 3 L/s O.K

## Slide 5
Example 6:
A network in which Q and hf refer to discharge and pressure drops respectively, subscripts 1, 2, 3, 4, and 5 designate respective values in pipe lengths AC, BC, CD, DA, AC, subscripts A B C & D designate discharges entering or leaving the junction points ABC& D respectively, by sticking the values given in the figure find the following discharges: QB, Q2, Q4 & Q5 and pressure drops hf4, hf5?

## Slide 6
-

## Slide 7
D) QD = Q3 + Q4
100= 40+ Q4 = 60
A) Q4 = QA+ Q1 + Q5
60=20 + 30+ Q5 = 10
C)Q3 + Q5 +Q2 =30
Q2 = 30 – 40 – 10 = -20
.B) Q1 + Q2 = QB
30+ 20= QB =50
∑ hf=0
@ ABC hf1- hf2 – hf5=0
60 – 40 – hf 5=0 hf 5 =20
Circuit ACD : hf4+ hf5 – hf3 =0
hf4 + 20 -120=0 hf4=100

## Slide 8
Branched pipeline
When three or more pipes meet at a junction then the following basics principles apply:
1-The continuity equation must be obeyed, the total flow into the junction must equal total flow out of the junction.
2-At any one point there can only be one value of head.
3- Darcyꞌs equation must be satisfied for each pipe.

## Slide 9
.
.
The water level A & B in two reservoir are 104.5 m and 100 m, above datum , a pipe joins each to a common point D where pressure is 9.8 KN /m2 gage, and height 83.4 above datum. Another pipe connects D to another tank. What will be the height of water level in C assuming the same values of f , and friction coefficient =0.0075, dia. of AD, BD, CD are 300, 450, and 600 mm , L=240, 270 and 300 m?

## Slide 10
.
D (pressure head)= = = 10 m
Piezometer head at D = 83.5+10= 93.5 m
Head loss between A & D =104.5 – 93.5 =11 m
= = = B& D = 100 -93.5 =6.5 m
Using Darcy Weisbach equation D ….. 11=
= =3m
BD…….6.5= = 2.66 m/s=v BD
Q1+Q2=Q3
QCD= (D2 * V+ D2 V= (0.32 * 3)+ (0.452 *2.66) =0.635 m3/s
VCD = Q/A = = 2.24 m/s
Head loss in CD = = = 3.84 m
C = 93.5 – 3.84 =89.66 m

## Slide 11
Thanks