## Slide 1: Fluid Mechanics Lectures 2nd year/2nd semister/2018-2019/Al-Mustansiriyah unv./College of engineering/Highway &Transportation Dep.Lec.1

## Slide 2
. Open channel flow
Definition:
Is the flow of a liquid in a conduit with free surface (surface is exposed to the atmosphere) , the conduit can have any cross section shape, but the fluid must be a liquid to provide the free surface. Fig.1 shows open channel flow that can be produced two ways, the channel that is open to the atmosphere over its entire length to produce a free surface. The conduit can also be closed along its length but open to the atmosphere at both ends and not running.

## Slide 3
.
)
Real world examples of open flow systems abound including those found in nature as well as those made artificially. Systems found in nature include rivers, creeks, and small streams. Examples of artificially made systems are canals, dam spillways, irrigation ditches, storm sewers, and rain gutters for buildings and roadsides. Factory applications include open channel used to carry cooling heating cleaning and mixing liquids for a variety of manufacturing and chemical processes.

## Slide 4
aspects | Open channel | pipe
Cause of flow | Gravity force(by bed slope) | The pipe must run full and the floe in general take place @ the expense of hydraulic pressure
Geometry (cross sec.) | May have any cross sec.shape: | Pipes generally round in cross sec.
Surface roughness | Varies between wide limits (it varies with depth of flow) | Roughness coefficient varies from a low value to a very high
Piezometric head | (z+y),y is the depth of flow,H.G.L coincide with the water surface. | Z+p/γ.p is the pressure in the pipe ,H.G.L does not coincide with the water surface.
velocity | The max. velocity occurs @ a little distance below the water surface. | The velocity distribution is symmetrical about the pipe axis. Max. velocity occurring @ the pipe center and the velocity @ the pipe wall reducing to zero.
Table 1 .Differences between flow in open and closed conduit:

## Slide 5
Types of channels:
1-Natural channels: rivers, streams.
2-Artificial channels: rectangular, trapezoidal.
3-Open channels( without cover): irrigation canals, rivers.
4-Coverd channels: partially filled conduits.
5-Prismatic channels: constant bed slope, same cross section.

## Slide 6
Types of flow:
1-Steady & unsteady flow:
When the depth, velocity and flow rate do not change with time the flow is steady, otherwise it is unsteady.
2-Uniform & non uniform:
If depth, slope, cross section and velocity constant over a given length of channel the flow is uniform, if not the flow is non-uniform.
3-Laminer & turbulent flow:
It depends on Reynolds no.
Re ˂ 500 Laminar
Re ˃ 2000 Turbulent
500 ˂ Re ˂2000 Transitional
4-Subcritical, critical, supercritical:
It depends on Froude no.:
Froude no.= V:velocity, D:hydraulic depth.
Fr ˂ 1 subcritical
Fr =1 critical
Fr ˃1 supercritical
-

## Slide 8
Definitions:
1-Depth of flow (y):It is the vertical distance of the lowest point of channel section from the free surface.
2-Depth of flow section : It is the depth of flow normal to the bed of channel.
Where ϴ = the angle of slope
D= y cos ϴ

## Slide 9
.
.
3- Top width (T):It is the width of the channel section at the free surface.
4-Wetted area (A): The cross section area of flow section of the channel.
5-Wetted perimeter P :The length of the channel boundary in contact with water.
6-Hydraulis radius R: The ratio of the cross section area to the wetted perimeter (R=A/P).

## Slide 10
.
For rectangular section:
R = =
For pipe section:
R= =
Or R=

## Slide 11
.
For trapezoidal section:
Area= Y(B+ZY)
P= B+ 2 Y

## Slide 12
Open channel formula for uniform flow:
1- Chezy's formula (Antoine Chezy 1775):
Q= A C
Q : rate of flow
A: cross section area
C: Chezys constant
R: Hydraulic radius
S: slope of channel bedC=

## Slide 13: table2
Surface kind | K
Smooth cement | 0.11
brick, concrete, wood | 0.21
Earth channels in very good condition | 1.54
Earth channel in rough condition | 3.17

## Slide 14
2- Manning's formula (Rober Manning 1889):
Q= R2/3 A
From which: c constant of Chezys' formula =

## Slide 15
Thanks