## Slide 2: Gates and Logic: Logic Gates and Logic Circuits

## Slide 3: Goals for Today
From Switches to Logic Gates to Logic Circuits
Logic Gates
  From switches
  Truth Tables
Logic Circuits
  Identity Laws
  From Truth Tables to Circuits (Sum of Products)
Logic Circuit Minimization
  Algebraic Manipulations
  Truth Tables (Karnaugh Maps)
Transistors (electronic switch)

## Slide 4: A switch
Acts as a conductor or insulator
Can be used to build amazing things…
The Bombe used to break the German
Enigma machine during World War II
Notes: Pictures show the Bombe built by Alan Turing to break the enigma machine ciphers.
They were Fixed-Program Computers came before stored-program computers (general purpose)
The former required re-wiring (e.g. ENIAC took 3 weeks to “re-wire”).

## Slide 5: Basic Building Blocks: Switches to Logic Gates
Either (OR)
Both (AND)
+
-
-
A | B | Light
OFF | OFF | 
OFF | ON | 
ON | OFF | 
ON | ON | 
A
B
A
B
A | B | Light
OFF | OFF | 
OFF | ON | 
ON | OFF | 
ON | ON | 
Truth Table
+
Notes: Speed and size of a mechanical switch

## Slide 6: Basic Building Blocks: Switches to Logic Gates
Either (OR)
Both (AND)
-
-
A
B
A
B
A | B | Light
OFF | OFF | 
OFF | ON | 
ON | OFF | 
ON | ON | 
A | B | Light
OFF | OFF | 
OFF | ON | 
ON | OFF | 
ON | ON | 
Truth Table
OR
AND
Notes: Speed and size of a mechanical switch

## Slide 7: Basic Building Blocks: Switches to Logic Gates
Either (OR)
Both (AND)
-
-
A
B
A
B
A | B | Light
0 | 0 | 
0 | 1 | 
1 | 0 | 
1 | 1 | 
A | B | Light
0 | 0 | 
0 | 1 | 
1 | 0 | 
1 | 1 | 
Truth Table
0 = OFF
1 = ON
OR
AND
Notes: Speed and size of a mechanical switch

## Slide 8: Basic Building Blocks: Switches to Logic Gates
Did you know?
George Boole Inventor of the idea of logic gates. He was born in Lincoln, England and he was the son of a shoemaker in a low class family.
A
B
A
B
OR
AND
Notes: E.g. logic statements:
“Jane will only go to the cinema tonight if a good film is on AND she has enough money.”
“Stuart will only go to the birthday party on Sunday if Katie OR Sujit is going too.”

## Slide 9: Takeaway
Binary (two symbols: true and false) is the basis of Logic Design
Notes: Add takeways at end of a block. Possibly build on takeaways throughout lecture

## Slide 10: Building Functions: Logic Gates
NOT:
AND:
OR:
Logic Gates
  digital circuit that either allows a signal to pass through it or not.
  Used to build logic functions
  There are seven basic logic gates:
  AND, OR, NOT,
  NAND (not AND), NOR (not OR), XOR, and XNOR (not XOR) [later]
A | B | Out
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 1
A | B | Out
0 | 0 | 0
0 | 1 | 0
1 | 0 | 0
1 | 1 | 1
A | Out
A
B
A
B
In
Notes: Flash Drives
Create truth table of AND or OR: state what they do

## Slide 11: Building Functions: Logic Gates
NOT:
AND:
OR:
Logic Gates
  digital circuit that either allows a signal to pass through it or not.
  Used to build logic functions
  There are seven basic logic gates:
  AND, OR, NOT,
  NAND (not AND), NOR (not OR), XOR, and XNOR (not XOR) [later]
A | B | Out
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 1
A | B | Out
0 | 0 | 0
0 | 1 | 0
1 | 0 | 0
1 | 1 | 1
A | Out
0 | 1
1 | 0
A
B
A
B
In
Notes: Flash Drives
Create truth table of AND or OR: state what they do
Did you know? Logic gates allow the computer to do things such as add, divide, multiply, do simple yes and no reasoning in certain situations along with other things.

## Slide 12: Building Functions: Logic Gates
NOT:
AND:
OR:
Logic Gates
  digital circuit that either allows a signal to pass through it or not.
  Used to build logic functions
  There are seven basic logic gates:
  AND, OR, NOT,
  NAND (not AND), NOR (not OR), XOR, and XNOR (not XOR) [later]
A | B | Out
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 1
A | B | Out
0 | 0 | 0
0 | 1 | 0
1 | 0 | 0
1 | 1 | 1
A | Out
0 | 1
1 | 0
A
B
A
B
In
A | B | Out
0 | 0 | 1
0 | 1 | 0
1 | 0 | 0
1 | 1 | 0
A | B | Out
0 | 0 | 1
0 | 1 | 1
1 | 0 | 1
1 | 1 | 0
A
B
A
B
NAND:
NOR:
Notes: Flash Drives
Create truth table of AND or OR: state what they do
Did you know? Logic gates allow the computer to do things such as add, divide, multiply, do simple yes and no reasoning in certain situations along with other things.

## Slide 13: Activity#1.A: Logic Gates
Fill in the truth table, given the following Logic Circuit made from Logic AND, OR, and NOT gates.
What does the logic circuit do?
a | b | Out
a
b
Out
Notes: Fill out table
Put, NOT, AND, OR labels in box

## Slide 14: Activity#1: Logic Gates
Fill in the truth table, given the following Logic Circuit made from Logic AND, OR, and NOT gates.
What does the logic circuit do?
a
b
d
Out
a | b | d | Out
0 | 0 | 0 | 
0 | 0 | 1 | 
0 | 1 | 0 | 
0 | 1 | 1 | 
1 | 0 | 0 | 
1 | 0 | 1 | 
1 | 1 | 0 | 
1 | 1 | 1 | 
Notes: Fill out table

## Slide 15: Goals for Today
From Switches to Logic Gates to Logic Circuits
Logic Gates
  From switches
  Truth Tables
Logic Circuits
  Identity Laws
  From Truth Tables to Circuits (Sum of Products)
Logic Circuit Minimization
  Algebraic Manipulations
  Truth Tables (Karnaugh Maps)
Transistors (electronic switch)

## Slide 16: Logic Gates
NOT:
AND:
OR:
XOR:
L
ogic Equations
  Constants: true = 1, false = 0
  Variables: a, b, out, …
  Operators (above): AND, OR, NOT, etc.
A | B | Out
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 1
A | B | Out
0 | 0 | 0
0 | 1 | 0
1 | 0 | 0
1 | 1 | 1
A | Out
0 | 1
1 | 0
A
B
A
B
In
A | B | Out
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 0
A
B
Notes: XOR is not a basic Logic Gate since it can be created from AND and OR gates, but it is often used as a basic Logic Operator

## Slide 17: Logic Gates
NOT:
AND:
OR:
XOR:
L
ogic Equations
  Constants: true = 1, false = 0
  Variables: a, b, out, …
  Operators (above): AND, OR, NOT, etc.
A | B | Out
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 1
A | B | Out
0 | 0 | 0
0 | 1 | 0
1 | 0 | 0
1 | 1 | 1
A | Out
0 | 1
1 | 0
A
B
A
B
In
A | B | Out
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 0
A
B
A | B | Out
0 | 0 | 1
0 | 1 | 0
1 | 0 | 0
1 | 1 | 0
A | B | Out
0 | 0 | 1
0 | 1 | 1
1 | 0 | 1
1 | 1 | 0
A
B
A
B
NAND:
NOR:
A | B | Out
0 | 0 | 1
0 | 1 | 0
1 | 0 | 0
1 | 1 | 1
A
B
XNOR:
Notes: XOR is not a basic Logic Gate since it can be created from AND and OR gates, but it is often used as a basic Logic Operator

## Slide 18: Logic Equations
NOT:
  out = ā = !a = a
AND:
  out = a ∙ b = a & b = a  b
OR:
  out = a + b = a | b = a  b
XOR:
  out = a  b = a + āb
Logic Equations
  Constants: true = 1, false = 0
  Variables: a, b, out, …
  Operators (above): AND, OR, NOT, etc.
Notes: Apologize that there are three ways to represent the same logic equation
XOR is not a basic Logic Gate since it can be created from AND and OR gates, but it is often used as a basic Logic Operator
AND is “product”
OR is “sum”
Read outloud

## Slide 19: Logic Equations
NOT:
  out = ā = !a = a
AND:
  out = a ∙ b = a & b = a  b
OR:
  out = a + b = a | b = a  b
XOR:
  out = a  b = a + āb
Logic Equations
  Constants: true = 1, false = 0
  Variables: a, b, out, …
  Operators (above): AND, OR, NOT, etc.
NAND:
  out = = !(a & b) =  (a  b)
NOR:
  out = = !(a | b) =  (a  b)
XNOR:
  out = = ab +
  .
Notes: Apologize that there are three ways to represent the same logic equation
XOR is not a basic Logic Gate since it can be created from AND and OR gates, but it is often used as a basic Logic Operator
AND is “product”
OR is “sum”
Read outloud

## Slide 20: Logic Manipulation
functions: gates ↔ truth tables ↔ equations
Example: (a+b)(a+c) = a + bc
a | b | c |  |  |  |  | 
0 | 0 | 0 |  |  |  |  | 
0 | 0 | 1 |  |  |  |  | 
0 | 1 | 0 |  |  |  |  | 
0 | 1 | 1 |  |  |  |  | 
1 | 0 | 0 |  |  |  |  | 
1 | 0 | 1 |  |  |  |  | 
1 | 1 | 0 |  |  |  |  | 
1 | 1 | 1 |  |  |  |  | 
Notes: (a+b)(a+c)
= aa + ab + ac + bc
= a + a(b+c) + bc
= a(1 + (b+c)) + bc
= a + bc