## Slide 1
Wind logarithm and power law profile
Basim Alknani

## Slide 2
Wind logarithmic profile in Statically Neutral and Non-Neutral Conditions:
To estimate the mean wind speed u(z), as a function of height, z, above the ground, we speculate that the following variables are relevant: surface stress (represented by the friction velocity, u*, and surface roughness (represented by the aerodynamic roughness length, z0. To determine wind speed at a height it is commonly expressed as follows:
Where is the elevation above the ground, is the surface roughness length, and ( =0.4) is von Karman constant . is defined as the friction velocity, where (ρ) is the density of the air and (τ) is the surface value of the shear stress. The roughness length describes the roughness of the ground or terrain where the wind is blowing. There are cases where wind speed is known at a reference height) and required at another in a case that can be derived from equation (1.5): (in neutral conditions)
The Businger –Dyer Relationships can be integrated with height to yield the wind speed profiles

## Slide 3
Where (L) is the Obukhov length and the function Ψ (𝑧/𝐿) is given for stable conditions (z/L > 0) by :
Ψ (𝑧/𝐿) = 4.7 (𝑧/ 𝐿) …………………….…………… 1.8
And for unstable (z/L < 0) by:
Ψ (𝑧/𝐿) = −2ln[(1+𝑥)/ 2] −ln[(1+𝑥2)/ 2] +2𝑡𝑎𝑛−1(𝑥)-𝜋 /2………………. 1.9
Where 𝑥 = [1− (15 𝑧/𝐿)]1/4.

## Slide 4
The Power-Law wind Profile
The power - law equation is a simple, yet a useful model of the vertical wind profile which was first proposed by Hellman (1916) . The power - law profile assumes that the ratio of wind speeds at different heights can be found by the following equation:
Where is the wind speed at a reference height (anemometer height), is the wind speed at a height (hub height), and (α) is the shear exponent (dimensionless parameter),itis found to depend on both the surface roughness and stability. the shear exponent also increases with increasing stability .

## Slide 6
HOMEWORK 1
Q1 ) write a mathematical expression of the following:
1- Wind speed logarithmic equation in stable conditions.
2- Wind speed logarithmic equation in unstable conditions.
3- Wind speed logarithmic equation in neutral conditions.
4- power-law equation for wind profile

## Slide 7
HOMEWORK 2
Q2 ) write a mathematical expression of the following:
1- The aerodynamic roughness length equation acceptable when the roughness elements are evenly spaced.
2- The aerodynamic roughness length equation which uses in an urban city
3- Displacement distance equation .
4- Friction velocity equation .
5- 𝑑𝑟𝑎𝑔 𝑐𝑜𝑒𝑓𝑓𝑖𝑐𝑖𝑒𝑛𝑡 equation .