## Slide 1: Computer Organization Arithmetic and logic Instructions Second Group Instructions
أعداد: م. د. سمر أميل يوسف
2026-2025

## Slide 2: Second Group Instructions
MUL, DIV REG
Memory
MUL instructions affect these flags only: CF, OF
When result is over operand size these flags are set to 1, when result fits in operand size these flags are set to 0.
For DIV flags are undefined.

## Slide 3: MUL instruction
when operand is a byte:
AX = AL * operand.
when operand is a word:
(DX AX) = AX * operand.

## Slide 4: MUL instruction
Q:Write a program in assembly language to compute Z= 5*3 put the result in cx?
MOV AL, 5
MOV Bl, 3
MUL Bl
mov cx,ax
RET

## Slide 5: MUL instruction
Q:Write a program in assembly language to compute Z= 4444H *2222H
MOV AX, 4444H
MOV CX, 2222H
MUL CX
RET

## Slide 6: MUL instruction
Q:Write a program in assembly language to compute Z= x*y , save the value in memory location [0000]
MOV AL, X
MOV BL, Y
MUL BL
MOV [0000] ,X
RET
X DB 8
Y DB 2

## Slide 7: Second Group Instructions
MUL, DIV REG
Memory
DIV flags are undefined.

## Slide 8
when operand is a byte:
AL = AX / operand
AH = remainder.
when operand is a word:
AX = (DX AX) / operand
DX = remainder.
DIV instruction

## Slide 9: DIV instruction
Q: Write a program in assembly language to compute Z=200 /4
MOV AX, 200
MOV BL, 4
DIV BL
RET

## Slide 10
Q: Write a program in assembly language to compute C=(FD/9)*(FA-32)
MOV AX,0FDH
MOV Bl,09
DIV Bl
MOV Bl,0FAH
MOV Cl, 32H
SUB Bl,Cl
MUL Bl
RET

## Slide 11: Q: Write a program in assembly language to compute [2518]=(8+5)/(FA*32)

## Slide 12
Q: Write a program in assembly language to compute the average of 5 degrees 80,88,90,80,88 ?
ADD AX,80
ADD AX,88
ADD AX,90
ADD AX,80
ADD AX,88
MOV BX,05
DIV BX
RET
Notes: mov cx, 5
sum:
add al,a1[si]
inc si
loop sum
mov bl,5
div bl
ret
a1 db 80H, 90H, 85H, 90H, 80H

## Slide 13: Third Group Instructions

## Slide 14: Third Group Instructions

## Slide 15
mov ax, 0FFFFH
neg ax
ret

## Slide 16
mov ax, 0FFFFH
NOT ax
ret