## Slide 1: Transmission Medium
Is the physical path between transmitter and receiver in a data transmission system.
Guided the waves are guided along a solid medium -copper twisted pair, -copper coaxial cable, and -optical fiber. | Unguided provide a means of transmitting electromagnetic signals but do not guide them - terrestrial microwave - Satellite Microwave - Broadcast Radio - Infrared

## Slide 2: Design Factors
Design factors relating to the transmission medium and to the signal determine the
data rate and
Distance,
Bandwidth.
Transmission impairments.
Interference and
Number of receivers.

## Slide 3: 1- Twisted Pair
The least-expensive and most widely-used guided transmission medium is twisted pair.
consists of two insulated copper wires arranged in a regular spiral pattern. A wire pair acts as a single communication link.
Neighboring pairs in a bundle typically have somewhat different twist lengths to reduce the crosstalk interference.
the twist length typically varies from two to six inches.
The wires in a pair have thicknesses of from 0.016 to 0.036 inches.

## Slide 4: twisted pair distance, bandwidth, and data rate.
is limited in all
For point-to-point analog signaling, a bandwidth of up to about 250 kHz is possible.
For long-distance digital point-to-point signaling, data rates of up to a few Mbps are possible
For very short distances, data rates of up to 100 Mbps have been achieved in commercially available products.

## Slide 5: Unshiealded and Shielded Twisted Pair
to improve the characteristics of this medium is to shield the twisted pair with a metallic braid or sheathing that reduces interference.
(STP) provides better performance at lower data rates.
it is more expensive and more difficult to work with than unshielded twisted pair.

## Slide 6: UTP Categories
Category 3. UTP cables and associated connecting hardware whose transmission characteristics are specified up to 16 MHz.
Category 4. UTP cables and associated connecting hardware whose transmission characteristics are specified up to 20 MHz.
Category 5. UTP cables and associated connecting hardware whose transmission characteristics are specified up to 100 MHz.
A key difference between Category 3 and Category 5 cable is the number of twists in the cable per unit distance. Category 5 is much more tightly twisted typically 3 to 4 twists per inch, compared to 3 to 4 twists per foot for Category 3.
The tighter twisting is more expensive but provides much better performance than Category 3.

## Slide 7: 2- Coaxial Cable
It consists of a hollow outer cylindrical conductor that surrounds a single inner wire conductor
The outer conductor is covered with a jacket or shield. A single coaxial cable has a diameter of from 0.4 to about 1 in.

## Slide 8: Coaxial Cable Applications
Most important of these are :
Television distribution
Long-distance telephone transmission
Short-run computer system links
Local area networks
For long-distance transmission of analog signals, amplifiers are needed every few kilometers.
The usable spectrum for analog signaling extends to about 400 MHz. For digital signaling, repeaters are needed every kilometer or so, with closer spacing needed for higher data rates.

## Slide 9: 3- Optical Fiber
An optical fiber is a thin (2 to 125 pm), flexible medium capable of conducting an optical ray. Various glasses and plastics can be used to make optical fibers.

## Slide 10: Optical Fiber Structure
An optical fiber cable has a cylindrical shape and consists of three concentric sections: the core, the cladding, and the jacket.
The core is the innermost section and consists of one or more very thin strands, or fibers, made of glass or plastic.
Each fiber is surrounded by its own cladding, a glass or plastic coating that has optical properties different from those of the core.
The outermost layer, surrounding one or a bundle of cladded fibers, is the jacket.
The jacket is composed of plastic and other material layered to protect against moisture, abrasion, crushing, and other environmental dangers.

## Slide 11: Optical Fiber Characteristics
The following characteristics
Greater capacity. The potential bandwidth, and hence data rate, of optical fiber is immense; data rates of 2 Gbps over tens of kilometers have been demonstrated.
Smaller size and lighter weight.
Lower attenuation.
Electromagnetic isolation. fiber is inherently difficult to tap.
Greater repeater spacing. Fiber transmission system that achieves a data rate of 3.5 Gbps over a distance of 318 km [PARK921 without repeaters. Coaxial and twisted-pair systems generally have repeaters every few kilometers.
Two different types of light source are used in fiber optic systems: the light emitting diode (LED) and the injection laser diode (ILD). Both are semiconductor devices that emit a beam of light when a voltage is applied.

## Slide 12: WIRELESS TRANSMISSION (Unguided)
For unguided media, transmission and reception are achieved by means of an antenna. For transmission, the antenna radiates electromagnetic energy into the medium (usually air), and for reception, the antenna picks up electromagnetic waves from the surrounding medium.
2-40 GHz (Microwave) Directional , 30MHz-1GHz (Radio waves)Omnidiractional Broadcasting radio, Infrared

## Slide 13: 1- terrestrial microwave
microwave antenna is the parabolic "dish 10 Feet
antenna is fixed rigidly ,achieve line-of-sight
Use in long-haul telecommunications service
requires far fewer amplif. or repeat. than coaxial
Use for short point-to-point links .
Common frequencies 2 to 40 GHz. Higher frequency means higher bandwidth and higher data rate.

## Slide 14: Frequencies and DataRates
Band (GHz) Bandwidth (MHz) Data rate (Mbps)
2 7 12
6 30 90
11 40 90
18 220 274
Repeaters or amplifiers, then, may be placed farther apart for microwave systems-10 to 100 km is typical. Attenuation increases with rainfall, the effects of which become especially noticeable above 10 GHz. Another source of impairment is interference.

## Slide 15: 2- Satellite Microwave
A communication satellite is, in effect, a microwave relay station.
It is used to link two or more ground-based microwave transmitter/receivers, known as earth stations, or ground stations. The satellite receives transmissions on one frequency band (uplink), amplifies or repeats the signal, and transmits it on another frequency (downlink). A single orbiting satellite will operate on a number of frequency bands, called transponder channels, or simply transponders.
To remain stationary, the satellite must have a period of rotation equal to the earth's period of rotation. This match occurs at a height of 35,784 km.
The communication satellite is a technological revolution as important as fiber optics. Among the most important applications for satellites are:
- Television distribution
- Long-distance telephone transmission
-Private business networks

## Slide 16: Applications and Characteristics
A recent development is the very small aperture terminal (VSAT) system, which provides a low-cost alternative. Figure 3.5 depicts a typical VSAT configuration.
The optimum frequency range for satellite transmission is 1 to 10 GHz. Below 1 GHz, there is significant noise from natural sources, including galactic, solar, and atmospheric noise, and human-made interference from various electronic devices.
Above 10 GHz, the signal is severely attenuated by atmospheric absorption and precipitation.
Most satellites providing point-to-point service today use 4/6 GHz bandwidth
The 12/14 GHz band has been
It is anticipated that this band will also saturate, and use is projected for the 19/29 GHz

## Slide 17: 3- Broadcast Radio
omnidirectional Antenna
Radio is a general term used to encompass frequencies in the range of 3kHz to 300 GHz.
broadcast radio to cover the VHF and part of the UHF band: 30 MHz to 1 GHz. This range covers FM radio as well as UHF and VHF television. This range is also used for a number of data-networking applications.
The range 30 MHz to 1 GHz is an effective one for broadcast communications. Unlike the case for lower-frequency electromagnetic waves, the ionosphere is transparent to radio waves above 30 MHz. Transmission is limited to line of sight, and distant transmitters will not interfere with each other due to reflection from the atmosphere. Unlike the higher frequencies of the microwave region, broadcast radio waves are less sensitive to attenuation from rainfall.

## Slide 18: 4- Infrared
Infrared communications is achieved using transmitters/receivers (transceivers) that modulate noncoherent infrared light. Transceivers must be in line of sight of each other, either directly or via reflection from a light-colored surface such as the ceiling of a room.
One important difference between infrared and microwave transmission is that the former does not penetrate walls. Thus, the security and interference problems encountered in microwave systems are not present. Furthermore, there is no frequency allocation issue with infrared, because no licensing is required.