## Slide 1: Essential notes in comet assay writing methods
Assist. Prof. Dr. zaynab s abdulghany
Molecular biology department
Iraqi center for cancer and medical genetics research
Mustansiriyah university

## Slide 2: Introduction
The alkaline comet assay is a technically simple, sensitive assay to detect DNA damage (strand breaks and other lesions that are converted into strand breaks under alkaline conditions)
international researchers have identified substantial variations in comet assay procedures and primary descriptors (such as %DNA in tail) between laboratories.
This variation could hamper inter-laboratory data comparison and interpretation, as well as attempts to standardize methods and promote the use of reference standards

## Slide 3
The main issue is that the comet assay does not directly measure the number of specific DNA lesions, but rather measures the migration of DNA in agarose gels as a result of the relaxation produced by strand breaks under alkaline conditions.
published comet assay studies often inadequately describe assay conditions. Even more troubling is the lack of data on positive experimental controls and positive assay controls, which are necessary for assessing assay performance
There is therefore an urgent need for a more comprehensive set of recommendations to describe comet assay conditions, including explanations for why certain steps need to be reported in detail.

## Slide 4: Minimum Information for Reporting Comet Assay (MIRCA)
to highlight key aspects of the comet assay procedure that must be described when reporting the results from cell culture studies, animal models, invertebrates, plants and human biomonitoring and clinical studies.
to ensure that specific information about the comet assay procedure is available to readers that will allow the results to be interpreted critically and compared with those from other studies.

## Slide 5
focus on the steps in the comet assay that may affect the level of DNA migration:
a physical effect that causes DNA to move faster in agarose irrespective of the absolute amount of DNA damage
increase the difference in DNA migration between unexposed and exposed specimens (i.e., detection of induced DNA damage)
Steps of alkaline comet assay:
isolation of cells and preparation of single-cell suspensions,
embedding of the cells in agarose,
cell lysis,
incubation of the nucleoids with lesion-specific enzyme (for the enzyme-modified comet assay) or with cell or tissue extract (for the in vitro DNA repair assay),
alkaline treatment,
electrophoresis,
neutralization,
staining and visualization
scoring and data analysis

## Slide 6: step 1 : isolation of cells
Notes | Reporting requirement | Comet assay parameter
The homogenization procedure (whether in buffer or medium) may affect levels of DNA damage. | Desirable | Preparation of a single-cell suspension (from solid tissue or cell culture)
For human biomonitoring studies, it should be specified whether the samples are whole blood (i.e., with erythrocytes), isolated leukocytes or peripheral blood mononuclear cells, or from which organ or tissue the cells are derived (buccal, sperm, etc.). | Essential | Cell type
Expected to be of little importance in most cases, but the gauge of needle and anticoagulant used might affect the level of DNA damage during cell isolation. | Desirable | Method for venipuncture and isolation of cells from blood (if cells were isolated)

## Slide 7
Notes | Reporting requirement | Comet assay parameter
The temperature and time period between isolation of cells and direct processing in comet assay (or cryopreservation) may affect the level of DNA damage. | Essential | Temperature and duration of transfer from isolation of cells to processing of cells
The freezing and thawing procedures might increase the basal level of DNA migration. For clinical intervention studies, it is essential to know whether samples taken at different times were analyzed fresh (i.e., in different experiments) or in the same comet assay experiment in the case of cryopreserved samples. | Essential | Storage (in case of specimens that have been cryopreserved)
Very few (if any) genotoxic agents give rise to DNA lesions that are repaired by only one DNA repair pathway; rather, most give rise to a spectrum of DNA lesions. The concentration/dose of the genotoxic agent should be reported. | Essential | Type of exposure used

## Slide 8
Notes | Reporting requirement | Comet assay parameter
Assay controls should always be included and reported in studies that do not have a positive control group. | Essential | Assay controls
Control groups are desirable (or even essential in certain cases). For most purposes, however (and especially in human biomonitoring), assay controls can replace negative and positive controls (i.e., control groups). | Desirable | Negative and positive controls

## Slide 9
Step 2 :Embedding the cells in the agarose
Notes | Reporting requirement | Comet assay parameter
Use of 2-gel versus 12-gel format, etc., might affect the level of DNA migration. | Desirable | Description of the type of slides
The final concentration (percentage after the cells have been added) is very important. As the concentration will change upon reuse of the agarose stock solution, it should be specified if it is used more than once. It is not informative enough to state the concentration of the stock solution. | Essential | Final concentration of low-melting-point-agarose containing cells

## Slide 10
Step 3 :lysis
Notes | Reporting requirement | Comet assay parameter
For buccal cells, an extra lysis step with proteinase K is needed. Lysis of sperm requires an incubation step with dithiothreitol and proteinase K to break disulfide bonds in the tightly packed DNA. | Essential | Buffer composition
The duration of the lysis can vary depending on the cell type. If it is too long, this may affect certain types of DNA lesions (e.g., conversion of alkali-stabile lesions to strand breaks), and if too short, lysis might be incomplete. It is important that the same duration is used in all experiments. | Desirable | Duration
Expected to have little effect on DNA migration, except in certain cases where alkali-stabile lesions may be converted to strand breaks. | Desirable | Temperature

## Slide 11
Step 4 :Alkaline electrophoresis
Notes | Reporting requirement | Comet assay parameter
The extent of DNA migration depends on the chemical composition. | Essential | composition
The extent of DNA migration is directly proportional to the strength of the electrophoretic field. | Essential | Voltage/cm over the slide support platform
The extent of DNA migration is directly proportional to the duration of electrophoresis. The duration is restricted to avoided overlap between comets. | Essential | Duration
Electrophoresis at high temperature might induce DNA strand breaks and thereby increase the level of DNA migration. | Essential | Temperature

## Slide 12
Step 5 :Neutralization
Notes | Reporting requirement | Comet assay parameter
No expected effect on DNA migration. | Desirable | composition

## Slide 13
Step 6 :Staining and visualization
Notes | Reporting requirement | Comet assay parameter
Dyes have different binding affinity to DNA and may therefore affect the calculation of primary comet assay descriptors in the image analysis software. | Essential | Type of DNA dye
Most likely does not affect the image analysis of the comets, but desirable information for researchers who want to repeat the specific protocol. | Desirable | Concentration of dye
Certain dyes may require incubation to produce a good fluorescent signal. | Desirable | Time from staining until microscopy
For image analysis by software, the DNA migration differs between magnifications. | Desirable | Microscope magnification
As the calculation of the %DNA in tail (or other descriptor) may be different between different image analysis systems, it is desirable to include images of comets and the level of DNA migration (e.g., as supplementary material or a citation to an earlier article with representative images, or by including images within figures). | Desirable | Representative images of comets

## Slide 14
Step 7 :Scoring and data analysis
Notes | Reporting requirement | Comet assay parameter
There are different ways to measure the level of DNA migration (i.e., %DNA in tail, tail length, tail moment and visual score). These primary comet assay descriptors have different scales, which cannot be directly compared. | Essential | Type of primary comet assay descriptor
Important because of low precision in the measurement of DNA in gels with few comets. | Essential | Number of comets scored per gel and number of gels scored
Using the mean versus median level of DNA migration might affect the estimate of DNA damage, depending on the distribution of comet scores. It is essential that authors clarify that mean/median values from comet distributions come from independent observations (i.e., different animals or humans, or cell culture experiments carried out on different days). | Essential | Measure of the central value of comet scores (e.g., mean or median when image analysis systems have been used for analysis of DNA migration)
Different software may have different algorithms for calculating primary comet assay descriptors. | Essential | Type of software for image analysis
The primary comet assay descriptor is a relative value (e.g., %DNA in the comet tail). Transformation to lesions per nucleotide or unaltered nucleobase pair is desirable for ease of comparisons between studies, although it does not affect the quality of the comet assay analysis. | Desirable | Calibration

## Slide 15
Step 8 :Statistical analysis of results
Notes | Reporting requirement
The statistical analysis should conform to standard practice for parametric, nonparametric or logistic regression, depending upon the study design. | Essential

## Slide 16: Conclusion
The MIRCA recommendations represent a standardized reporting checklist for the description of comet assay procedures and results. However, this is not a guide to best-practice procedures for the assay.
The MIRCA recommendations provide an important tool to aid researchers, reviewers and editors in ensuring that the comet assay is performed rigorously and reported comprehensively.
Taken together, these will increase the quality and impact of comet assay results in scientific studies.